#include <stdio.h>

#include <cuda.h>

#define MATRIXSIZE 480*480

#define XYLENGTH   480

#define BLOCK_LENGTH 16

#define AR_INDEX(ar , a, b) (ar[ a*XYLENGTH + b ])

//declaration of the matrices used in the host memeory

float* h_ga;

float* h_dz;

float* h_ez;

float* h_hx;

float* h_hy;

float* h_ihx;

float* h_ihy;

float* h_gi2;

float* h_gj2;

float* h_gi3;

float* h_gj3;

float* h_fi1;

float* h_fj1;

float* h_fi2;

float* h_fj2;

float* h_fi3;

float* h_fj3;

//declaration of the matrices used in the kernal

__device__ float* d_ga;

__device__ float* d_dz;

__device__ float* d_ez;

__device__ float* d_hx;

__device__ float* d_hy;

__device__ float* d_ihx;

__device__ float* d_ihy;

__device__ float* d_gi2;

__device__ float* d_gj2;

__device__ float* d_gi3;

__device__ float* d_gj3;

__device__ float* d_fi1;

__device__ float* d_fj1;

__device__ float* d_fi2;

__device__ float* d_fj2;

__device__ float* d_fi3;

__device__ float* d_fj3;

// Kernel that executes on the CUDA device

__global__ void UpdateDZfield(int time)

{

// the coordinate for sinusoidal source

int ic = XYLENGTH /2 -5;

int jc = XYLENGTH /2 -5;

float ddx = 0.01;     // cell size

float dt = ddx / 6e8;  // time step

float pulse;

float pi = 3.14159;

//Block index

int bx = blockIdx.x;

int by = blockIdx.y;

// Tread index

int tx = threadIdx.x;

int ty = threadIdx.y;

// coordinates location in the global matrix

int x = bx * BLOCK_LENGTH + tx;

int y = by *BLOCK_LENGTH + ty;

if( x== 0 || y ==0){

// boundary conditions do nothing

}else{

// update the dz field

AR_INDEX(d_dz, x, y) = d_gi3[x] * d_gj3[y]* AR_INDEX( d_dz, x, y)

+ d_gi2[x]* d_gj2[y] * 0.5 *( AR_INDEX( d_hy, x ,y) - AR_INDEX( d_hy, x-1 ,y)

- AR_INDEX( d_hx, x ,y) + AR_INDEX( d_hx, x ,y-1) );

}

// sinusoidal sources

pulse = sinf(2*pi*1500*1e6*dt*time);

if( x ==ic && y ==jc)

AR_INDEX(d_dz, x, y) = pulse;

} // end of the UpdateDZfield(int time)

__global__ void UpdateEZfield( )

{

//Block index

int bx = blockIdx.x;

int by = blockIdx.y;

// Tread index

int tx = threadIdx.x;

int ty = threadIdx.y;

// coordinates location in the global matrix

int x = bx * BLOCK_LENGTH + tx;

int y = by *BLOCK_LENGTH + ty;

//calculation of EZ field

AR_INDEX(d_ez, x, y) = AR_INDEX(d_ga, x, y) * AR_INDEX(d_dz, x,y);

//set the Ez edges to 0, as part of the PML

if( x==0 || x == (480-1) || y==0 || y==(480-1))

AR_INDEX(d_ez,x,y) = 0.0;

}// end of the UpdateEZfield( )

__global__ void UpdateHfield( )

{

float curl_e;

//Block index

int bx = blockIdx.x;

int by = blockIdx.y;

// Tread index

int tx = threadIdx.x;

int ty = threadIdx.y;

// coordinates location in the global matrix

int x = bx * BLOCK_LENGTH + tx;

int y = by * BLOCK_LENGTH + ty;

//calculation of Hx field

if(y == (480-1)) {

// the boundary condition,do nothing

} else{

curl_e = AR_INDEX(d_ez, x,y) - AR_INDEX(d_ez, x,y+1);

AR_INDEX(d_ihx, x, y) = AR_INDEX(d_ihx, x, y) + d_fi1[x]* curl_e;

AR_INDEX(d_hx, x, y) = d_fj3[y]* AR_INDEX(d_hx,x,y) + d_fj2[y]*0.5*(curl_e + AR_INDEX( d_ihx,x,y) );

}

//calculation of Hy field

if(x == (480-1)) {

// the boundary condition ,do nothing

}else{

curl_e = AR_INDEX(d_ez, x+1,y) - AR_INDEX(d_ez, x,y);

AR_INDEX(d_ihy, x, y) = AR_INDEX(d_ihy, x, y) + d_fj1[y]* curl_e;

AR_INDEX(d_hy, x, y) = d_fi3[x]* AR_INDEX(d_hy,x,y) + d_fi2[x]*0.5*(curl_e + AR_INDEX( d_ihy,x,y) );

}

}  // end of the UpdateHfield( )

// main driver that executes on the host

int main(void)

{

// declare variables used in FDTD simulation

int l, n ,i , j, nsteps, npml,T;

float ddx, dt,epsz, pi, epsilon, sigma, eaf;

float xn, xxn, xnum, xd, curl_e;

float t0, spread;

//assign a file to record the result

FILE *fp,*fopen();

// allocate host memory for matrices and arrays

unsigned int mem_size_matrix = sizeof(float) * MATRIXSIZE;

h_ga = (float*) malloc(mem_size_matrix);

h_dz = (float*) malloc(mem_size_matrix);

h_ez = (float*) malloc(mem_size_matrix);

h_hx = (float*) malloc(mem_size_matrix);

h_hy = (float*) malloc(mem_size_matrix);

h_ihx = (float*) malloc(mem_size_matrix);

h_ihy = (float*) malloc(mem_size_matrix);

unsigned int mem_size_array = sizeof(float) * XYLENGTH;

h_gi2 = (float*) malloc(mem_size_array);

h_gj2 = (float*) malloc(mem_size_array);

h_gi3 = (float*) malloc(mem_size_array);

h_gj3 = (float*) malloc(mem_size_array);

h_fi1 = (float*) malloc(mem_size_array);

h_fj1 = (float*) malloc(mem_size_array);

h_fi2 = (float*) malloc(mem_size_array);

h_fj2 = (float*) malloc(mem_size_array);

h_fi3 = (float*) malloc(mem_size_array);

h_fj3 = (float*) malloc(mem_size_array);

// allocate device memory for matrices and arrays

cudaMalloc( (void**) & d_ga, mem_size_matrix);

cudaMalloc( (void**) & d_dz, mem_size_matrix);

cudaMalloc( (void**) & d_ez, mem_size_matrix);

cudaMalloc( (void**) & d_hx, mem_size_matrix);

cudaMalloc( (void**) & d_hy, mem_size_matrix);

cudaMalloc( (void**) & d_ihx, mem_size_matrix);

cudaMalloc( (void**) & d_ihy, mem_size_matrix);

cudaMalloc( (void**) & d_gi2, mem_size_array );

cudaMalloc( (void**) & d_gj2, mem_size_array );

cudaMalloc( (void**) & d_gi3, mem_size_array );

cudaMalloc( (void**) & d_gj3, mem_size_array );

cudaMalloc( (void**) & d_fi1, mem_size_array );

cudaMalloc( (void**) & d_fj1, mem_size_array );

cudaMalloc( (void**) & d_fi2, mem_size_array );

cudaMalloc( (void**) & d_fj2, mem_size_array );

cudaMalloc( (void**) & d_fi3, mem_size_array );

cudaMalloc( (void**) & d_fj3, mem_size_array );

//assign the value to the variables declared

epsz = 8.8e-12;

// initialize the matrix

for( i =0; i< XYLENGTH ; i++) {

for( j =0; j< XYLENGTH;j++){

AR_INDEX(h_dz , i , j)=  0.0;

AR_INDEX(h_ez , i , j)=  0.0;

AR_INDEX(h_hx , i , j)=  0.0;

AR_INDEX(h_hy , i , j)=  0.0;

AR_INDEX(h_ihx , i , j)= 0.0;

AR_INDEX(h_ihy , i , j)= 0.0;

AR_INDEX(h_ga , i , j) =  1.0;

} // end inner for loop

} // end outer for loop

// calculate the PML parameters

for( i=0;i<XYLENGTH; i++){

h_gi2[i] = 1.0;

h_gi3[i] = 1.0;

h_fi1[i] = 0.0;

h_fi2[i] = 1.0;

h_fi3[i] = 1.0;

h_gj2[i] = 1.0;

h_gj3[i] = 1.0;

h_fj1[i] = 0.0;

h_fj2[i] = 1.0;

h_fj3[i] = 1.0;

}

//Ask for the Number of PML cells for calcualtion

printf("Number of PML cells ---->");

scanf("%d", &npml);

for( i =0; i <= npml; i++){

xnum = npml -i;

xd = npml;

xxn = xnum/xd;

xn = 0.33 *pow(xxn,3);

h_gi2[i] = 1.0 / (1.0 + xn);

h_gi2[XYLENGTH-1-i] = 1.0 /(1.0 + xn) ;

h_gi3[i] = (1.0 -xn)/ (1.0 +xn);

h_gi3[XYLENGTH-1-i] = (1.0 -xn)/ (1.0 +xn);

xxn = (xnum -.5) /xd;

xn = 0.25 * pow(xxn,3);

h_fi1[i] = xn;

h_fi1[XYLENGTH-2-i] =xn;

h_fi2[i] = 1.0 / (1.0 + xn);

h_fi2[XYLENGTH-2-i] = 1.0 /(1.0 + xn) ;

h_fi3[i] = (1.0 -xn)/ (1.0 +xn);

h_fi3[XYLENGTH-2-i] = (1.0 -xn)/ (1.0 +xn);

}

for( j =0; j<=npml; j++){

xnum = npml -j;

xd = npml;

xxn = xnum /xd;

xn = 0.33 * pow(xxn, 3);

h_gj2[XYLENGTH-1-j] = 1.0 /(1.0 + xn) ;

h_gj3[j] = (1.0 -xn)/ (1.0 +xn);

h_gj3[XYLENGTH-1-j] = (1.0 -xn)/ (1.0 +xn);

xxn = (xnum -.5) /xd;

xn = 0.25 * pow(xxn,3);

h_fj1[j] = xn;

h_fj1[XYLENGTH-2-j] =xn;

h_fj2[j] = 1.0 / (1.0 + xn);

h_fj2[XYLENGTH-2-j] = 1.0 /(1.0 + xn) ;

h_fj3[j] = (1.0 -xn)/ (1.0 +xn);

h_fj3[XYLENGTH-2-j] = (1.0 -xn)/ (1.0 +xn);

}

// simulation set up

t0 = 40.0;

spread = 15.0;

T = 0;

nsteps = 1;

//copy the matrices and arrays from host memory to device memory

cudaMemcpy(d_dz,h_dz, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_ez,h_ez, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_hx,h_hx, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_hy,h_hy, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_ga,h_ga, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_ihx,h_ihx, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_ihy,h_ihy, mem_size_matrix ,cudaMemcpyHostToDevice);

cudaMemcpy(d_gi2,h_gi2, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_gj2,h_gj2, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_gi3,h_gi3, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_gj2,h_gj2, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_fi1,h_fi1, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_fj1,h_fj1, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_fi2,h_fi2, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_fj2,h_fj2, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_fi3,h_fi3, mem_size_array,cudaMemcpyHostToDevice);

cudaMemcpy(d_fj3,h_fj3, mem_size_array,cudaMemcpyHostToDevice);

//kernal dimensions setup

dim3 dimBlock  (BLOCK_LENGTH, BLOCK_LENGTH);

dim3 dimGrid   (XYLENGTH / BLOCK_LENGTH , XYLENGTH / BLOCK_LENGTH);

//start simulation

while(nsteps >0){

printf("nsteps -->");

scanf("%d", &nsteps);

printf("%d\n", nsteps);

for ( n =1; n <= nsteps; n++){

T = T+1;

UpdateDZfield <<< dimGrid , dimBlock >>> ( T ) ;

cudaThreadSynchronize();

UpdateEZfield <<< dimGrid , dimBlock >>> ( );

cudaThreadSynchronize();

UpdateHfield <<< dimGrid , dimBlock >>> ( );

cudaThreadSynchronize();

} // end for loop

} // end while loop

//copy d_ez back to h_ez and record into file

cudaMemcpy(h_ez, d_ez, mem_size_matrix ,cudaMemcpyDeviceToHost);

//cudaMemcpy(h_hx, d_hx, mem_size_matrix ,cudaMemcpyDeviceToHost);

// write the E field out to a file "Ez"

fopen_s(&fp,"Ez.txt", "w" );

for(j=0;j< XYLENGTH;j++){

for(i=0;i< XYLENGTH;i++) {

fprintf(fp, "%6.3f ", AR_INDEX(h_ez,i,j));

} // end inner for loop

fprintf( fp," \n");

} // end outer for loop

/*

// write the d_hx field out to a file "Ez"

fopen_s(&fp,"Hx", "w" );

for(j=0;j< XYLENGTH;j++){

for(i=0;i< XYLENGTH;i++) {

fprintf(fp, "%6.3f ", AR_INDEX(h_hx,i,j));

} // end inner for loop

fprintf( fp," \n");

} // end outer for loop

*/

// close the file

fclose(fp);

// clear host and device memories

free(h_ez);

free(h_dz);

free(h_hx);

free(h_hy);

free(h_ihx);

free(h_ihy);

free(h_ga);

free(h_gi2);

free(h_gj2);

free(h_gi3);

free(h_gj3);

free(h_fi1);

free(h_fj1);

free(h_fi2);

free(h_fj2);

free(h_fi3);

free(h_fj3);

cudaFree(d_ez);

cudaFree(d_dz);

cudaFree(d_hx);

cudaFree(d_hy);

cudaFree(d_ihx);

cudaFree(d_ihy);

cudaFree(d_ga);

cudaFree(d_gi2);

cudaFree(d_gj3);

cudaFree(d_fi1);

cudaFree(d_fj1);

cudaFree(d_fi2);

cudaFree(d_fj2);

cudaFree(d_fi3);

cudaFree(d_fj3);

system("pause");

}